## Slide 1: EDES 301 Dog Treat Dispenser Proposal
09/30/2024
Aden Briano

## Slide 2: Background Information
  Inspiration: Dog Treat Dispenser W/Arduino
  Packages to use: Adafruit
Is your dog tired of having to sit or lie down to receive a treat? Do they want something more stimulating? Well I’ve got them covered! I’m going to make a treat dispenser box with a flywheel launcher and treat feeder mechanism lying on top. In front of the box there will be a large blue button and a large yellow button with a same colored LED above, embedded into the wall of the box. When the test subject barks at the box, a random LED will light up, and the test subject is required to press the corresponding button in 15 seconds to launch a treat (which they can then chase after). The box will need to be barked at again to restart the process.

## Slide 3: System Block Diagram
PocketBeagle
PWM/GPIO
P2_1
Logic Shifter
Motor Shield
DC Motors
Yellow Button
Blue Button
GPIO
P2_2
GPIO
P2_4
USB
USB Mic

## Slide 4: Power Block Diagram
PocketBeagle
PWM/GPIO
P2_1
Logic Shifter
~3.3V ~5mA
~5V ~5mA
Motor Shield
DC Motors
~5V ~150mA
~5V
Yellow Button (Product ID 1186)
Blue Button (Product ID 1186)
~5V
P2_13
VOUT
USB Port
USB Mic
~5V
P2_13
VOUT

## Slide 5: Components / Budget
Component | EDES301 to Buy? | Cost
Continuous Rotation Motors | Yes | $26.99
L298N Motor Driver | Yes | $6.99
Blue and Yellow Button | No | $20
USB Microphone | No | $7.96
Logic Shifters | No | $7.99